## Slide 1: DIGITAL DESIGN AND COMPUTER ARCHITECTURE
COURSE OUTCOME 1 PROJECT

## Slide 2: PROJECT TITLE:
DESIGNING AND SIMULATION OF HALF-ADDER AND FULL-ADDER CIRCUITS

## Slide 3: PRESENTED BY:
1. NIKHIL SRIVATSA-2620090029
2. SRI VISHWA CHAITANYA-2620090036
3. DARAPU VINOD KUMAR-2620090068
4. JASWANTH POORNA SAI-2620090097

## Slide 4: PROJECT OBJECTIVES
Understand Binary Addition Basics
  Grasp the fundamental principles of binary addition and how logic gates implement arithmetic operations.
Design a Half Adder Circuit
  Construct a half adder using XOR and AND gates to perform single-bit addition without a carry input.
  Verify its correctness using a truth table.
Design a Full Adder Circuit
  Extend the half- adder design to include a carry-in input, combining two half -adders and an OR gate.
  Demonstrate accurate addition of three binary inputs.

## Slide 5: BASIC CONCEPT
HALF ADDER CIRCUIT
Purpose: Adds two single-bit binary numbers (A and B).
Inputs: A, B
Outputs:
  Sum (S) → Generated using an XOR gate (A ⊕ B)
  Carry (C) → Generated using AND gate (A · B)
Concept:
  The XOR gate gives the sum because it outputs 1 only when the inputs differ.
  The AND gate gives the carry because a carry occurs only when both inputs are 1.
FULL ADDER CIRCUIT
Purpose: Adds three single-bit binary numbers (A, B, and Carry-in).
Inputs: A, B, Cin
Outputs:
  Sum (S) → (A ⊕ B) ⊕ Cin
  Carry (Cout) → (A · B) + (Cin · (A ⊕ B))
Concept:
  Built using two Half Adders and an OR gate.
  The first Half Adder adds A and B.
  Second Half Adder adds the Sum from the first stage with Cin.
  The OR gate combines the carry outputs to produce Cout.

## Slide 6: INPUT COMPONENTS AND OUTPUT DESCRIPTION
HALF ADDER
Inputs:
A → First single-bit binary input
B → Second single-bit binary input
Outputs:
Sum (S) → Produced by XOR gate (A ⊕ B)
  Output is 1 when inputs differ (A=0, B=1 or A=1, B=0).
Carry (C) → Produced by AND gate (A · B)
  Output is 1 only when both inputs are 1.
Description: The Half Adder performs addition of two bits but does not account for a carry-in from a previous stage.
FULL ADDER
Inputs:
A → First single-bit binary input
B → Second single-bit binary input
Cin (Carry-in) → Carry input from a previous addition
Outputs:
Sum (S) → (A ⊕ B) ⊕ Cin
  Output is 1 when an odd number of inputs are 1.
Carry-out (Cout) → (A · B) + (Cin · (A ⊕ B))
  Output is 1 when at least two inputs are 1.
Description: The Full Adder extends the Half Adder by including a carry-in, making it suitable for chaining multiple adders to perform multi-bit binary addition

## Slide 7: LOGIC DESIGN FOR HALF ADDER CIRCUIT
Component | Symbol | Function | Logic Expression
Input 1 | A | First binary digit | —
Input 2 | B | Second binary digit | —
XOR Gate | ⊕ | Produces the Sum output | 
AND Gate | · | Produces the Carry output | 
Component | Symbol | Function | Logic Expression
Input 1 | A | First binary digit | —
Input 2 | B | Second binary digit | —
XOR Gate | ⊕ | Produces the Sum output | 
AND Gate | · | Produces the Carry output | 

## Slide 8: LOGIC DESIGN FOR FULL ADDER CIRCUIT
Component | Symbol | Function | Logic Expression
Input 1 | A | First binary digit | —
Input 2 | B | Second binary digit | —
Input 3 | Cin | Carry input from previous addition | —
XOR Gates | ⊕ | Produce the Sum output | 
AND Gates | · | Generate intermediate carries | and
OR Gate | + | Combine carries to produce Carry-out | 
Component | Symbol | Function | Logic Expression
Input 1 | A | First binary digit | —
Input 2 | B | Second binary digit | —
Input 3 | Cin | Carry input from previous addition | —
XOR Gates | ⊕ | Produce the Sum output | 
AND Gates | · | Generate intermediate carries | 
OR Gate | + | Combine carries to produce Carry-out | 

## Slide 9: HALF ADDER CIRCUIT LOGIC OUTPUT

## Slide 10: TRUTH TABLE OF HALF ADDER CIRCUIT

## Slide 11: FULL ADDER CIRCUIT LOGIC OUTPUT

## Slide 12: TRUTH TABLE FOR FULL ADDER CIRCUIT

## Slide 13: EXPECTED RESULT FOR HALF ADDER
When both inputs are 0, the output is Sum = 0, Carry = 0.
When one input is 1 and the other is 0, the output is Sum = 1, Carry = 0.
When both inputs are 1, the output is Sum = 0, Carry = 1.

## Slide 14: EXPECTED RESULT FOR FULL ADDER
Sum is 1 when an odd number of inputs are 1.
This ensures correct addition of three binary inputs (A, B, and Cin).
Carry-out (Cout) is 1 when at least two inputs are 1.

## Slide 15: THANK YOU